## Slide 1
Topic
Applications of Fuzzy Sets

## Slide 2
Applications of Fuzzy Sets
Reasoning tool like Fuzzy Logic Controller
Fuzzy Clustering
Fuzzy Mathematical Programming
Fuzzy Graph theory
Others

## Slide 3
Fuzzy Logic Controller (FLC)
Developed by Mamdani and Assilian around 1975
Performance depends on Knowledge Base (KB), which consists of Data Base (DB) and Rule Base (RB)
The performance of an FLC largely depends on the RB and optimizing the DB is a fine tuning process

## Slide 4
Two Forms of FLC
Linguistic Fuzzy Modeling: High interpretability and Low accuracy.
Ex: Mamdani Approach
Precise Fuzzy Modeling: Low interpretability and High accuracy.
Ex: Takagi and Sugeno’s Approach

## Slide 5
Mamdani Approach
An FLC consists of four modules: Rule Base; Inference Engine; Fuzzification; De-fuzzification

## Slide 6
Steps Involved in the Working Cycle of FLC
Identify the condition ( also known as antecedent ) and action (also called consequent) variables of the process
Fuzzification: Measurements of input variables are converted into appropriate fuzzy sets to express measurement uncertainties

## Slide 7
Inference Engine uses fuzzified measurements to evaluate the control rules stored in the fuzzy rule base
De-fuzzification: Fuzzified output is then converted into a single crisp value

## Slide 8
Fuzzy Reasoning Process
Rule1: IF S1 is A1 AND S2 is B1 THEN f’ is C1
Rule2: IF S1 is A2 AND S2 is B2 THEN f’ is C2

## Slide 9
Let S1* and S2* are the inputs for fuzzy variables S1 and S2
Firing strengths of the first and second rules can be calculated as follows:

## Slide 10
Membership value of the combined control action C is given by

## Slide 11
De-fuzzification Methods
where : firing area of -th rule
: center of the area
: No. of fired rules
Center of Sums Method

## Slide 12
Methods of De-fuzzificztion

## Slide 13
where : No. of small areas or regions
: Area of -th small region
: Center of area of -th small region
Centroid Method

## Slide 14
From the membership function distribution of combined control action, the range of the output variable corresponding to the maximum value of membership is identified. The mid-value of this range is considered to be the crisp output of the controller.
Mean of Maxima Method

## Slide 15
Numerical example (Mamdani Approach)
Let us consider a problem scenario related to navigation of a mobile robot in the presence of four moving obstacles. Obstacle 2 is found to be the most critical one. Our aim is to develop a fuzzy logic-based motion planner that will be able to generate the collision-free path for the robot. There are two inputs, namely the distance between the robot and the obstacle (D) and angle () for the motion planner and it will generate one output, that is, deviation. Distance is represented using four linguistic terms, namely Very Near (VN), Near(NR), Far(FR) and Very Far (VFR), whereas the input: angle and output: deviation are expressed with the help of five linguistic terms, such as Ahead (A), Ahead Left (AL), Left (LT) Ahead Right(ART) and Right (RT).

## Slide 17
The data base (DB) and rule base (RB) of the FLC are shown below.

## Slide 18
Determine the output: deviation for the set of inputs: distance D=1.04 m and angle = , using Mamdani Approach. Use different methods of defuzzification.

## Slide 19
Solution:
Inputs: Distance = 1.04 m; Angle =
Distance of 1.04 m may be either NR or FR, Angle of
To determine the membership, corresponding to the distance = 1.04 m.

## Slide 20
Distance of 1.04 m may be called NR with and FR with
Similarly, Angle of may be declared A with and ART with
Fired rules are as follows:
If Distance is NR AND Angle is A Then Deviation is RT
If Distance is NR AND Angle is ART Then Deviation is A
If Distance is FR AND Angle is A Then Deviation is ART
If Distance is FR AND Angle is ART Then Deviation is A

## Slide 21
Strengths ( VALUES) of the fired rules:
429

## Slide 22
Fuzzified outputs:

## Slide 23
Union of the fuzzified outputs:

## Slide 24
Methods of Defuzzification
1. Center of Sums Method

## Slide 26
2. Centroid Method

## Slide 28
3. Mean of Maxima

## Slide 29
A rule is composed of fuzzy antecedent and functional consequent parts
i-th rule can be represented as follows:
If x1is Ai1 and x2 is Ai2 ….. and xn is Ain then
yi=ai0+ai1 x1+……….+ain xn
Takagi and Sugeno’s Approach

## Slide 30
where a0, a1, …….., an are the coefficients
A non-linear system is considered to be a combination of several linear systems
Weight of i-th rule can be determined as follows:
wi = μiA1(x1) μiA2(x2)……… μiAn(xn)

## Slide 31
Combined control action can be determined as follows:
where k indicates the total number of rules.

## Slide 32
Numerical example (Takagi and Sugeno’s Approach
A fuzzy logic-based expert system is to be developed that will work based on Takagi and Sugeno’s approach to predict the output of a process. The DB of the FLC is shown below. As there are two inputs: and and each input is represented using three linguistic terms (for example, LW, M, H for and NR, FR, VFR for ) there is a maximum of 3 x 3 = 9 feasible solutions. The output of the i-th rule, that is, is expressed as follows:

## Slide 33
Where and
If is found to be LW, M and H, respectively;
and if is seen to be NR, FR and VFR, respectively. Calculate the output of the FLC for the inputs: =6.0, =2.2

## Slide 35
Inputs: =6.0, = 2.2
Inputs: of 6.0 unit may be called LW or M.
Inputs: of 2.2 unit may be called FR or VFR.
Determination of membership value:
Solution:

## Slide 36
Using the principle of similar triangle

## Slide 37
Input of 6.0 may be called LW with μLW =0.8
Input of 6.0 may be called M with μM =0.2
Similarly, Input of 2.2 may be called FR with μFR =0.8
Input of 2.2 may be called VFR with μVFR =0.2

## Slide 38
is LW and is FR
is LW and is VFR
is M and is FR
is M and is VFR
Fired Set of Inputs

## Slide 39
Weights

## Slide 40
Functional consequent values
6

## Slide 41
Output,

## Slide 42
Let us assume that a process having n inputs (I1,I2,……In) and one output (that is, O) is to be modeled using an FLC
Hierarchical Fuzzy Logic Controller

## Slide 43
Let us also assume that m linguistic terms (fuzzy sets) are used to represent each variable.
Total no. of rules = mn
Problem : curse of dimensionality

## Slide 44
To overcome this problem, we go for Hierarchical Fuzzy Logic Controller
Total no. of rules = m2(n-1)

## Slide 45
To determine the importance of input variable towards the output
Sensitivity
We carry out experiment by varying the input variables through different amounts, say 0.1%, 1.0%, 10.0% etc. and recording the outputs of the controller
Sensitivity Analysis
Methods to Determine Sensitivity

## Slide 46
2.O = f(I1, I2)
We change the input I1 by a small amount δI1 and determine the change in output using Mean-Value theorem

## Slide 47
Where lies between I1 and I1+δI1
If then δO > δI1
Thus, the contribution of I1 on the output O can be determined.

## Slide 48
Potential tool for dealing with imprecision and uncertainty
Does not require an extensive mathematical formulation of the problem
Advantages of FLC

## Slide 49
Designing a proper KB of an FLC is a difficult task
May not be suitable for modeling a process involving many variables
Disadvantages of FLC